## Slide 1
Rapid Cross Platform DSP with the ARM Cortex M4
Eli Hughes
ehughes@wavenumber.net

## Slide 2: Presentation Scope
In the “trenches” perspective.
DSP Evolution, history and application rationale
Quick introduction to the Cortex M4
Vendors & tool-chains
Look at some “interesting” instructions
CMSIS-DSP library
Performance stats
Some fun demos

## Slide 3: Digital Signal Processing
DSP is an application of discrete math to digital systems
One doesn’t necessarily need a special chip to implement a DSP algorithm
I can implement DSP on an 8051…. Or an abacus…. It just might not be as fast or as sophisticated as I would like it to be
I can also choose to implement a 2 tap FIR running at 1Hz sample rate with 4-bit data on a $5000 FPGA

## Slide 4: The Evolution of DSP Hardware
FPGA / Logic
Time
Dedicated High End “DSP” Chip (ADI SPARC, TI C6000)
Dedicated “Low End” Chip (Microchip DsPIC, Freescale DSP56F)
32-BIT MCU
16-BIT MCU
8-BIT MCU
DSP’ometer
0
Truckloads
Sun goes “supernova”
Abacus
6s?

## Slide 5: The 6s
DSP has traditionally been relegated to specialized processors and architectures.
There exists a large number of DSP applications that don’t require an expensive FPGA or high-end specialized chip.
Many applications also need the standard IO (USB, Ethernet, etc.)
The M4 can be useful for many applications. Keep in mind it is still general purpose RISC. Lots of register manipulation!

## Slide 6: Applications
IIR Filter on a dynamic sensor / accelerometer
A matched filter to detect an event
Some sort of frequency domain analysis
Real time control systems, low/mid range audio….
Can’t do it with 8051…. need USB, Ethernet, etc. Maybe need moderate sample rates.

## Slide 7: Application Example – “Play Node”
Consider a “box” to implement networked sounds, sensors and lighting.
Boxes are distributed over a large area (25m x 25m).
A master controller communicates with the nodes to form a cool outdoor “games space”

## Slide 8: Application Example – “Play Node”
Requirement #1 - The worlds most rugged and inexpensive input device…. “The Acoustic Button” (Need 4 Channels)
Notes: 4aa

## Slide 9: Application Example – “Play Node”
Requirement #2 - Sound Playback – 44.1KHz – 4 Channels .wav or .mp3
Requirement #3 - Embedded FAT File system on USB Thumb Drive…. USB Mass Storage Class Host
Requirement #4 - Lighting Control for WS2812 or APA102 “smart” LEDs. Control effects on chains of 100’s of pixels at 30FPS
Requirement #5 – CAN Bus communications

## Slide 10: Application Example – “Play Node”
Requirement #6 – USB Device input - Mass storage Class to configuration file system
Requirement #7 – Misc Inputs (4-20mA)
Requirement #8 – Instant Boot & Real Time…. No Linux
Requirement #9 - Can’t burn watts of Power

## Slide 11: Application Example – “Play Node”
Lots of requirements…. Some light DSP + Audio + USB + CAN + Standard I/O
Cortex M4 fits well….. (This case used the LPC43x Series)

## Slide 12: ARM Cortex?
Who here is familiar with ARM Cortex?
3 Families
  A Applications Processors - High-end cell phone/tablet chips
  R Real Time - Lock-step/real-time automotive, high-end control
  M Microcontroller - Focused on lower cost 32-bit. I.E. A good reason to move from 8/16-Bit.

## Slide 13: ARM Cortex?
Why does Cortex M Exist?
-To fix the architectural problems in the ARM7TDMI
I.E. A better interrupt system, common internal elements, bit-banding, thought-out API to CPU
http://community.arm.com/docs/DOC-2607

## Slide 14: IRQ Latency….
The IRQ latency & nesting in the Cortex M allows for reasonable “sample by sample processing”. Control loops, real time IIR, etc.
Input
Output
Dt

## Slide 15: ARM Cortex M4
M3 + DSP instructions + Optional hardware floating point
2 Variants: M4 and M4F (hardware floating point)

## Slide 16: The “Bible”
http://infocenter.arm.com/help/index.jsp
  Cortex M4 Technical Reference Manual
  Cortex M4 Devices Generic User Guide

## Slide 17: When Looking for help….
Silicon vendors generally do not provide the ARM documentation for their implementation.
The vendor reference manuals document vendor peripherals and implementation notes. I.E. IRQ slot assignments.
Details on the core CPU is found in the arm technical reference manuals…
Good news is that ARM provides abstraction to the core functions. Easy to move to other vendors.

## Slide 18: Lots of Silicon Available
Freescale, NXP, Atmel, Texas Instruments, EFM Micro, Spansion, Analog Devices, ST….. Just about everyone except Microchip!
We can get everything from a 3mm x 3mm package to a BGA256 between the vendors. Lots of variety in IO, peripherals, etc…
Speeds from 20MHz to 240MHz

## Slide 19: Some Notable Implementations
NXP LPC43xx -- Good “digital” implementation. Multiple cores, SGPIO, SCT, ROM bootloaders, 204MHz….
Freescale Kinetis - Great ADCs. Embedded wireless options. Lot’s of choice across ARM Cortex M4.
Analog Devices – Motor controller / power analysis variants. SINC3 Filters… Great ADCs, direct connection to isolated ADCs
Make sure to look at everyone…. Lot’s of variety in packages, peripherals, etc.

## Slide 20: Toolchains
KEIL, IAR  If cost is not an Issue
“Vendor” Tools  Freescale Codewarrior, Kinetis Design Studio, NXP LPCXpresso, TI Code Composer. Most are free or free to start. Eclipse + GCC+ Debugger. KDS is a “pure” open tool chain.
ATMEL Studio 6  Microsoft Visual Studio as a front end to GCC
Rowley Crossworks  Proprietary GUI front end for GCC
Other GCC based front-ends. (CooCox, Code Sourcery….)
Cobble together GCC, GDB, Open OCD etc. on your own https://launchpad.net/gcc-arm-embedded

## Slide 21: Low Cost Dev Boards
Freescale FRDM $($15-$30)
NXP LPCXpresso ($25-$40)
Atmel Xplained ($30-$40)
ST Discovery ($15 - $30)
TI Launch Pad ($15-$30)

## Slide 22: Let’s Talk Bare Metal
Assembly language programming not required BUT…..
  You should take a look at the instruction set
  Some real gems in the manual….
  You need to think about YOUR algorithm and how it will map.
  You need to be familiar with your compiler and optimization levels.
  You need to be familiar with the documentation
  http://infocenter.arm.com/help/index.jsp

## Slide 23: Some Interesting Instructions
Integer: UMLAL and SMLAL
Multiply, with optional Accumulate, using 32-bit operands and producing a 64-bit result.
http://infocenter.arm.com/help/topic/com.arm.doc.dui0553a/DUI0553A_cortex_m4_dgug.pdf
Using these we can have IIR filters with 64-bit precision in the accumulation / State Variables.

## Slide 24: High Precision Filter Using SMLAL
x[n-1]
x[n-2]
b[0]
b[1]
y[n-2]
b[2]
Z-1
x[n]
Z-1
a[2]
a[1]
y[n-1]
Output Formatting
Z-1
Z-1
X
S
X
S
X
S
X
S
X
S
Green = 32-bit Orange = 64-bit Purple = User Defined
Input
Output
Good for filters where Fo << Fs.
Very low filter noise
I.E. IIR Audio BiQuad with Low Cutoff
SMLAL

## Slide 25: Some Interesting Instructions
SMUAD and SMUSD
Signed Dual Multiply Add and Signed Dual Multiply Subtract
16-bit FFT Butterfly
Fast FIR,IIR  You can process multiple 16-bit taps at one time

## Slide 26: Some Interesting Instructions
VLMA, VLMS ,VNMLA, VNMLS, VNMUL
Multiplies two floating-point values, and accumulates or subtracts the results . Floating-point multiply with negation followed by add or subtract.
For floating point filters. Note that with SMLAL we can get more precision with the integers!
Floating Point Note: Your toolchain may *not* have the FPU initialized in the C startup routines.

## Slide 27: Do I need to write assembly code?
Sometimes it is useful. I have found the SSAT instruction useful in many cases.
Some of the instructions can be inferred in C code
  acc += (q63_t) x2 * b2
  Will compile to an SMLAL (with the right optimization levels!)
q31_t
q63_t

## Slide 28: Cortex Microcontroller Software Interface Standard CMSIS

## Slide 29: Kicking the CMSIS Tires
CMSIS Code can be acquired here:
http://www.arm.com/products/processors/cortex-m/cortex-microcontroller-software-interface-standard.php
Open source…. Easy to look at. Let’s look at the package

## Slide 30: Some Library Fundamentals
Fixed Point Data types
  Q0.7 Q0.15 Q0.31 Q0.63
    Defined data types used a fixed point scaling normalized from -1 to 1
    Some functions output other fixed point scalings (FFT)
    *most* functions have a Q0.15 and Q0.31 version for data inputs. Some use internal resolutions at Q0.63 or Q1.62 for high precision
    Documentation does a good job an indicating when you need to scale, saturation, etc.
Floating Point – 32-Bit IEEE 754. (Some M7’s will support doubles in future)

## Slide 31: Filtering Functions
IIR, FIR, Interpolation, Decimation…..
Post shift to implement coefficients > 1
Pay attention to coefficients
Let’s look into the docs

## Slide 32: Frequency Domain
Real & complex FFTs
DCT
Bit reversed ordering options
Let’s look in the documentation….. Lots to talk about…

## Slide 33: Building the CMSIS Library
CMSIS includes Keil uVision build example projects.
You should learn how to build the library from scratch.
  Lots of options –> optimization levels, compiler flags, etc.

## Slide 34: Building the CMSIS Library
SoftABI
  Single precision floating point operations are implemented in hardware and hence provide a large performance increase over code that uses traditional floating point library calls, but when calls are made between functions any floating point parameters are passed in ARM (integer) registers or on the stack.
  SoftABI is the 'most compatible' as it allows code that is not built with hardware floating point usage enabled to be linked with code that is built using software floating point library calls.
http://www.support.code-red-tech.com/CodeRedWiki/CM4_FloatingPoint

## Slide 35: Building the CMSIS Library
HardABI
  Single precision floating point operations are implemented in hardware, and floating point registers are used when passing floating point parameters to functions.
  HardABI will provide the highest absolute floating point performance, but is the 'least compatible' as it means that all of the code base for a project (including all library code) must be built for HardABI.
http://www.support.code-red-tech.com/CodeRedWiki/CM4_FloatingPoint

## Slide 36: CMSIS Library Performance
LPC-LINK-2 as an evaluation board for NCP LPC4370 @204MHz – Triple Core (CortexM4 + 2 Cortex M0).
RAM only Device. Can get close to ideal performance
LPCXPRESSO4337 – eval board ($25) for LPC4337. Dual Core (Cortex M4F + Cortex M0). Flash based.
These are high end implementations of the M4. We can use them to develop scaling equations for RAM based and FLASH based execution

## Slide 37: CMSIS Library Performance – Test Methodology
We want to get a measure of “clock cycles” to execute code. (not time). We can use this to scale to other CPUs
LPC43xx Timer 0 can run at core rate. 32-bit
Reset Timer0, Start Timer0  Stop Timer0 Read Timer0 value
  This is our “overhead” in clock cycles to measure function execution
Reset Timer0 Start Timer 0->Execute DSP CodeStop Timer 0 Read Timer0 and subtract “overhead”
Between the RAM based and Flash based platforms, we should get some real world profiles.

## Slide 38: CMSIS Library Performance – Test Methodology
Real and complex FFT at varying block sizes for Q15, Q31 and float.
IIR Filter – high precision Q0.31, Q0.15 and float
FIR Filter – high precision Q0.31 , Q0.15 and float
Eli’s per sample high precision Q0.31 BiQuad
Look at different optimization Levels (O0,O1,O2,O3,Og,Os) and SoftABI vs HardABI
Code available on GITHUB
https://github.com/ehughes/ESC-M4

## Slide 39: CMSIS Library Performance – Test Methodology
Now for the results…. Let’s look at Eli’s spreadsheet!

## Slide 40: Some Fun Applications/Demonstrations
Active Pickguard
http://www.2pl-1.com/active-pickguard/

## Slide 41: Some Fun Applications/Demonstrations
MonkeyJam
https://community.freescale.com/docs/DOC-100149

## Slide 42: Some Fun Applications/Demonstrations
MonkeyListen
https://community.freescale.com/docs/DOC-100207

## Slide 43: M4 to the M7
The Cortex M7 was recently release with a handful of vendor implementation.
M4 is limited by memory access (No Caches)
M7 has different pipeline, Cache and tightly coupled memory
M7 has a variant for double precision floating point
M7 is very new…. Some silicon implementations (ST, Atmel, Freescale). M4 has a lot selection. Come back next year!

## Slide 44: Questions and Discussion